## Slide 1
ARL ParaPower Fundamentals
Dr. Lauren Boteler, Dr. Mike Fish, Mr. Morris Berman
U.S. Army Research Laboratory

## Slide 2: Outline
ARL ParaPower Fundamentals
Features
Material Types
Internal Boundary Cavities (IBCs)
Time Varying Heating
ParaPower Code Structure
Convergence

## Slide 3: Codesign – Parametric Analysis (ParaPower)
ARL’s ParaPower tool
Compact 3D thermal resistance and stress network model
Quickly analyze large multi-disciplinary parameter space
>100X faster solution time with reasonable accuracy
Simple node temperature and stress output
Problem Statement: It is critical that the time required to understand a complete multi-disciplinary parametric space is reduced, this will eliminate overdesign in power modules and improve SWaP-C.
Objective: Develop a thermal transient tool that can support the military and the industry to quickly develop optimized power packages.
Notes: Current SOA:
  CAD tools can do feedback (ex. ANSYS Workbench) but large parametric space is difficult
  Work in co-design at the chip level (TSV, TTSV, microchannel, electrical co-design)
  Electro-mechanical work at the board level
  No work in power modules or to the level proposed
  ARL has published work on the thermal aspect

## Slide 4: ParaPower Finite Difference
Single Node Resistance Network
  p = time step number
  n = number of elements
  Δt = time step (sec)
  ρ = density
  cp = specific heat
  V = element volume
Thermal capacitance term

## Slide 5: ParaPower Finite Difference
Single Node Resistance Network
To move from timestep to :
Previous t.s.
DOF
Boundary Conductance
Matrix
Ambient Temperature Vector
Element Heating
Steady
Conductance
Matrix
Sensible Heat Capacity
New temperature DOF vector
In a model with solid elements

## Slide 6: Integrate stress into model
Combine
Thermal Analysis & Stress Analysis
Single Node Resistance Network
Hsueh, C. H., “Thermal Stress in Elastic Multilayer Systems,” Thin Solid Films, vol 418, pp 182 – 188, 2002.
E – Modulus of elasticity
α –CTE
c – Uniform component of strain
tb – Bending axis location
z – Vertical location in the substrate/film stack
r – Radius of curvature
Bending Strain
Total Strain
Stress in the substrate:
Stress in individual film layers:
Network nodes confined to single material
Can vary number of nodes in each material
Stress model is substrate dependent (significant thickness and dominates stress model), appropriate for power electronics.

## Slide 7: Outline
ARL ParaPower Fundamentals
Features
Material Types
Internal Boundary Cavities (IBCs)
Time Varying Heating
ParaPower Code Structure
Convergence

## Slide 8: Feature Based GUI
Transitioned the GUI from Layers to Features

## Slide 9: fEATURES
Everything is defined as a feature, each feature is subdivided into elements and each element comprises a 3D resistor network.
Feature 1
Feature 2
Element

## Slide 10: Features
Each feature is defined by
(X1, Y1, Z1) and (X2, Y2, Z2)
Material
Heat
Num X, Num Y, Num Z

## Slide 11: Features Continued
Subsequent features overwrite previous features
All divisions intersect each other
  Can put divisions on largest elements and then nothing else
Error trapping to remove any feature that is >2 orders of magnitude smaller than the smallest feature

## Slide 12: Outline
ARL ParaPower Fundamentals
Features
Material Types
Internal Boundary Cavities (IBCs)
Time Varying Heating
ParaPower Code Structure
Convergence

## Slide 13: Materials database

## Slide 14: 4 types of materials
Solid
Stress properties: CTE, E, nu
Thermal solid phase properties: thermal conductivity, density, specific heat
PCM
Solid properties +
Thermal liquid phase properties: thermal conductivity, density, specific heat
Latent heat
Melting temperature
IBC
Ambient temperature
Heat transfer coefficient

## Slide 15: Outline
ARL ParaPower Fundamentals
Features
Material Types
Internal Boundary Cavities (IBCs)
Time Varying Heating
ParaPower Code Structure
Convergence

## Slide 16: New feature: IBCs
Internal Boundary Cavities (IBCs)
  Features that are defined by a heat transfer coefficient and an ambient temperature
  Used for heat sinks, voids, etc.
  Allows
    heat sinks anywhere
    Agnostic geometries
Internal node:
IBC node:

## Slide 17: IBC Example locations
Agnostic Geometries
Heat Sinks/Internal Channels

## Slide 18: IBC heat sinks

## Slide 19: Agnostic Geometries
Due to the nature of the solver, the entire box must be defined. Any volume not defined is automatically defined as adiabatic
If adiabatic is not desirable, simply put a bounding box of an IBC that is the desired condition
Undefined volume defaults to adiabatic
Surrounding is IBC defined as h=10 and T=20

## Slide 20: Validating IBC results
Interior regions that can be designated as fluid volumes
Modeled as a bulk fluid temp and htc
Comparison with SolidWorks FlowSim conjugate model
1 htc averages extracted and applied to ParaPower FD model
Good agreement (2% )
Surface temperature of heated component
20 °C fluid inlet

## Slide 21: Interior Voids
Foundation of correlation-based internal convection
and htc updated explicitly
Surface temperature heatsink baseplate
20 °C fluid inlet

## Slide 22: Outline
ARL ParaPower Fundamentals
Features
Material Types
Internal Boundary Cavities (IBCs)
Time Varying Heating
ParaPower Code Structure
Convergence

## Slide 23: Applying heat
When defining features, optionally define a heat (Q) in Watts
  Volume = W/cm3
  Plane = W/cm2
Can add a zero thickness layer to get a W/cm2
7mm x 7mm chip with 100W of heat → 204W/cm2

## Slide 24: Results from set up
Each feature outputs a temperatures versus time plot
5 second run time
  0.1 sec time step
  1000 iterations
  h_wall = 300

## Slide 25: Detailed visual results
The temperature versus time plot is generated automatically, detailed visual results are also available at all time steps

## Slide 26: Time dependent heating/cooling
There are 3 types of heating conditions
  Scalar
  Function (t)
  Table
Defined individually for each feature

## Slide 27: Time dependent heating/cooling

## Slide 28: Outline
ARL ParaPower Fundamentals
Features
Material Types
Internal Boundary Cavities (IBCs)
Time Varying Heating
ParaPower Code Structure
Convergence

## Slide 29: ARL Parapower code structure Current Datastructures
Basic GUI Flow
TestCaseModel Structure
External Conditions
Features
Parameters
Material Database
Structure
Function
FormModel.m
MaterialDatabase
ModelInformation Structure
Geometry
Heat Source Q(t)
BC’s
Material Database
ParaPowerThermal.m
Results
Temperature (t)
MeltFraction (t)
Stress Model (dir)
Visualize.m
Results
Stress (t)
Save
TestCaseModel
ModelInformation
Stress
Temperature
MeltFraction
GUI Operation

## Slide 30: Formmodel.m
  Input
  ExternalConditions on each model face
    ambient temperature
    heat flux
  Features
    rectangular volumes
    specified X, Y, Z divisions define element size
    heat source (constant or time dependent)
  Parameters
    time stepping
    initial temperature
    processing temperature (not currently used to compute prestress)
  Materials
    3 Types: solid, phase change material, internal boundary condition
    stored in encapsulated database with distinct GUI and independent load/save abilities
  Function
  Translate individual features into a single unified geometry

## Slide 31: Solvers
ParaPowerThermal
Compute temperature and melt fraction states over given time steps
  Input
  Geometry - single matrix with each element having an identified material type
  Heat source – single matrix of function handles that define Q(t) for each element
  Boundary conditions – includes time vector
  Material library – carries material properties and element initialization and behavioral characteristics based on type
stress_MinerV1
Initial stress model computes stress state as a function of time
  Input
  Same as above
  Temperature states

## Slide 32: Visualize
Provides for flexible visualization of ModelInformation and state information.
Rotatable/Scalable
Dynamic or fixed color scale
Any material can be
  Solid elements
  Edge only element
  Single face of element (left, front, etc)
  Masked
Element transparency adjustable
Linearly interpolated or single color per element

## Slide 33: ARL parapower code structure in-process updates
Code is under GIT version control hosted at a DoD repository
Materials, TestCase, ModelInformation, Results being reformulated into objects
  Increased flexibility (element types: IBC, supercooling, etc)
  Improved implicit program documentation
  Maintainability
  Data Encapsulation
  Shared codebase with Simulink compatibility
Simulink Integration
  Solver implemented as Matlab system object
  Programmatic model definition
  Model Input – IBC boundary temps
  Model Output – IBC heat flux

## Slide 34: Outline
ARL ParaPower Fundamentals
Features
Material Types
Internal Boundary Cavities (IBCs)
Time Varying Heating
ParaPower Code Structure
Convergence

## Slide 35: PCM Melt Validation
0.48 | 0.24 | 0.12 | 0.06 | 0.03 | 0.02 | 0.01 | 0.01 | 0.01
1.06 | 0.53 | 0.28 | 0.14 | 0.07 | 0.04 | 0.02 | 0.01 | 0.01
2.76 | 1.34 | 0.70 | 0.35 | 0.18 | 0.09 | 0.05 | 0.03 | 0.02
8.85 | 4.31 | 2.25 | 1.10 | 0.54 | 0.28 | 0.14 | 0.08 | 0.04
31.88 | 15.94 | 8.26 | 4.03 | 1.98 | 1.01 | 0.51 | 0.27 | 0.14
126.37 | 60.83 | 32.12 | 17.48 | 7.78 | 3.98 | 1.94 | 1.05 | 0.51
545.17 | 265.07 | 136.65 | 65.08 | 33.52 | 17.14 | 8.49 | 4.40 | 2.13
2468.87 | 1246.23 | 613.01 | 308.17 | 159.32 | 78.46 | 38.93 | 20.29 | 9.62
12611.26 | 6451.08 | 3165.98 | 1618.00 | 807.28 | 401.21 | 204.77 | 103.01 | 50.44
Convergence time (sec)
ParaPCM tool compared to ANSYS simulation results (<5% error in 1 sec)
1D ARL PCM

## Slide 36: Compare to exact 1D solution: Timestep
Error metrics and runtime for different timesteps
1ms →
ΔT = 0.09°C
runtime = 2ms
100ms →
ΔT = 1°C
runtime = 0.04ms
Notes: If a linear problem, the order of convergence should be 1 (linear problem) , there is a diminishing return to smaller timestpes – this is unexpected if a linear problem.

## Slide 37: Compare to exact 1D solution: grid spacing
L2 norm and runtime for grid spacing
0.01mm →
Max ΔT = 0.02°C
RMS ΔT = 0.05°C
runtime = 3 ms
1mm →
Max ΔT = 4°C
RMS ΔT = 2°C
runtime = 1 ms
Notes: Discretization error is no longer linked to